# Multi-Analog Output with a Raspberry Pico
Out of the need for an unexpensive Multi- Analog- Output Board this idea came up:
A Raspi Pico receives a serial string via serial line and transfers the numeric values to Microchip MCP4802, which are connected in parallel to an SPI bus with multiple CS (Chip Select) signals.
This as a proof of concept to mayby later cascade these Picos like neopixels with a serial chain connection protocol.
## Setup
The pico is set up as descripted in USB Keyboard and Gamepad Emulation for an old analog Joystick
## The Software
import sys import time import board import busio import digitalio from adafruit_bus_device.spi_device import SPIDevice # list of available chip select signals chip_select_ports=[board.GP13] # define the conversion values to write values to outputs # value max , output mask multiplier, output mask flags, byte size, endian coding output_channels =[ {'max':0xFF , 'mult':16 , 'flags' : 0x1000 , 'size' : 2 , 'endian' : 'big' }, {'max':0xFF , 'mult':16 , 'flags' : 0x9000 , 'size' : 2 , 'endian' : 'big' } ] chip_selects=list(map(lambda port: digitalio.DigitalInOut(port), chip_select_ports)) # assessing the cs ports with busio.SPI(board.GP10, MOSI=board.GP11) as spi_bus: devices = list(map(lambda cs: SPIDevice(spi_bus, cs), chip_selects)) # assessing the cs ports print('Start- please remember that the first input line can contain garbage...') for line in sys.stdin: line=line.strip() values=line.split() value_counter=-1 for device in devices: for channel in output_channels: value_counter += 1 if value_counter>= len(values): break this_val=values[ value_counter ].strip() try: val_out = int( this_val ) val_out &= channel['max'] # mask out everything > max except: val_out=0 bytes_out = (channel['flags'] | (val_out * channel['mult'] ) ).to_bytes(channel['size'],channel['endian']) # The object assigned to spi in the with statements below # is the original spi_bus object. We are using the busio.SPI # operations busio.SPI.readinto() and busio.SPI.write(). #bytes_read = bytearray(4) #with device as spi: # spi.readinto(bytes_read) with device as spi: print('send', ''.join('{:02x}'.format(x) for x in bytes_out), val_out) spi.write(bytes_out)

## The Hardware
: Where is the schematics?